## Slide 1: ELECTROMECHANICAL SYSTEM
Chapter 2: dEFiNITION and Principle of motor operationS

## Slide 2: MOTOR CONTROL A motor control circuit can be defined as a means of supplying power to and removing power from a motor.

## Slide 3: Electric motor
It is a machine which converts electric energy into mechanical energy or work and requires electric energy input.

## Slide 4: Two Types of Electric motors
DC Motor
AC Motor

## Slide 5: 1. DC Motors
Operate on Direct Current from a battery or DC power supply.
They work on the principle that a conductor in a magnetic field experiences a mechanical force.

## Slide 6: 1. DC Motors

## Slide 7: 1. DC Motors
3 Basic Parts
Armature – The rotating part with wire coils around a core and a shaft that rotates on bearings.
Stator – The stationary part containing coils of wire.
Commutator – Terminated points on the armature where brushes make contact to transfer current from stationary to rotating parts.

## Slide 8: 1. DC Motors
4 Basic types of DC motors
Permanent Magnet DC Motor – Uses a magnet for field flux.
Advantages: Excellent starting torque and good speed regulation.
Disadvantages: Limited load capacity, typically used in low horsepower applications; torque is limited to 150% of rated torque to avoid magnet demagnetization.

## Slide 9: 1. DC Motors
4 Basic types of DC motors
2. Series DC Motor – Provides high starting torque.
Advantages: Capable of moving large shaft loads when first energized.
Feature: Field winding and armature are connected in series

## Slide 10: 1. DC Motors
4 Basic types of DC motors
Shunt DC Motor – Field winding is connected in parallel with the armature.
Feature: Field windings consist of many turns of wire.

## Slide 11: 1. DC Motors
4 Basic types of DC motors
4. Compound DC Motor – Combines series and shunt motor features.
Series Field Winding: Connected in series with the armature.
Shunt Field Winding: Connected in parallel with the armature.
Benefits: Combines high torque and regulated speed.

## Slide 12: 1. DC Motors
DC Motors for Mobile Robots
1. Brushed DC motor - Uses permanent magnets in the rotor and electromagnets in the stator.
Commutator: Detects rotor orientation and flips the current using brushes.
Function: Brushes rotate with the rotor to maintain current flow and motor operation.

## Slide 13: 1. DC Motors
DC Motors for Mobile Robots
2. Geared DC motor - DC motor coupled with gears to increase torque while reducing speed.
Application: Commonly used in robots to pull weight and components.
Gear Mechanism: Motor shaft connects to gears, decreasing rpm and increasing torque.

## Slide 14: 1. DC Motors
DC Motors for Mobile Robots
3. Brushless DC motors - Rotor uses permanent magnet, stator uses electromagnet, and Hall Effect sensors detect rotor orientation.
Advantages: Higher torque and greater speed than brushed motors, ideal for robots.
Disadvantages: Expensive due to design complexity, requires a controller for speed and rotation.

## Slide 15: 1. DC Motors
DC Motors for Mobile Robots
4. Servo Motors - DC motors with feedback control circuitry, gear system, and position sensing (potentiometer).
Function: Moves motor shaft to a desired position based on control signal (pulse).
Rotation: Limited to a specific range (usually 200°); can be modified for continuous rotation.
Wiring: Requires three wires: Ground, Power, and Control pulse.

## Slide 16: 1. DC Motors
DC Motors for Mobile Robots
5. Stepper motors - Brushless motors that divide rotation into discrete steps with electrical pulses.
Function: Rotates in steps per revolution, jumping each step with a pulse.
Torque: Similar to brushed DC motors but with less torque.
Feedback: No complex position feedback required.

## Slide 17: 1. DC Motors
DC Motors for Mobile Robots
6. Linear DC motor - Stator unwrapped into a flat coil track.
Function: Rotor moves in a straight line over the stator.

## Slide 18: 2. AC Motors
Convert AC electrical power into mechanical power.
Operate on Alternating Current, oscillating between positive and negative.
Principle: Interaction between the revolving magnetic field in the stator and the opposing magnetic field in the rotor.

## Slide 19: 2. AC Motors

## Slide 20: 2. AC Motors
Basic Parts
Stator – fixed outer portion
Rotor – spins inside the AC motor
Air gap – Space between stator and rotor where energy is transferred via induction.

## Slide 21: 2. AC Motors
Classifications
According to their principle of operation
a. Synchronous motor
b. Asynchronous motor
Induction motors
Squirrel cage induction motor
Wound-rotor induction motor

## Slide 22: 2. AC Motors
Classifications
Commutator motor
Series motor – single phase, universal
Compensated motor – conductively, inductively
Shunt motor – single, compensated
Repulsion motor – straight, compensated
Repulsion-start induction motor
Repulsion induction motor

## Slide 23: 2. AC Motors
Classifications
2. According to the type of current
a. single phase
b. three-phase
3. According to their speed
a. constant speed
b. variable speed
c. adjustable speed

## Slide 24: 2. AC Motors
Classifications
4. According to their structural features
a. Open
b. Enclosed
c. Semi-enclosed
d. ventilated
e. Pipe – ventilated
f. Riverted frame

## Slide 25: 2. AC Motors
Types of AC Motors
Synchronous Motors – Speed remains constant with increasing load.
Asynchronous Motors – Speed varies with increasing load.

## Slide 26: Characteristic of an induction motor
Induction (Asynchronous) Motor:
AC motor where rotor current is induced electromagnetically by the stator's magnetic field.
No electrical connection to the rotor is needed.

## Slide 27: Characteristic of an induction motor
Advantages
It has a simple, robust and almost unbreakable construction
It requires minimum care and maintenance
Its cost is low and is very reliable
It has a sufficiently high efficiency
It has a reasonably good power factor
It is self starting

## Slide 28: Characteristic of an induction motor
Disadvantages
Its speed cannot be varied without loss of efficiency
Its speed decreases with the increase of load
Its has somewhat an inferior starting torque

## Slide 29: General types of induction motors
Squirrel cage induction motor
Its rotor is self-contained and resembles a squirrel cage. The rotor conductors are permanently short-circuited by end-rings.

## Slide 30: General types of induction motors
Wound rotor or phase wound or rotor induction motor or slip-ring motors
Its rotor has insulated coils of wire and resembles a DC armature. The rotor conductors are connected to slip rings and shorted thru the brushes.

## Slide 31: Distinction between Squirrel cage and wound rotor induction motors
Squirrel cage induction motor | Wound Rotor Induction Motor
Copper losses is low | Copper losses is high
Starting torque is low but running torque is good | Starting torque is higher than squirrel cage induction motor
Efficiency is high due to low resistance | Efficiency is low
Speed can be varied by changing poles | Speed can be varied very slightly by changing the extra rotor resistance
Speed is nearly constant but slightly falls with load | More speed falls with load
Starting current is high | Starting current is low
Applications: Printing machine Flour mills Saw mills Lathe Blower mills | Applications: Rolling mills Flour mills Lifts Crane erector

## Slide 32: REferences
Pertuzella, F. D. (2010). Electric Motors and Control Systems (1st ed.). New York: McGraw-Hill
http://www.robotplatform.com/knowledge/actuators/dc_motors.html

## Slide 33: END of Chapter 2